## Slide 1: Resilient Datacenter Load Balancing in the Wild
Hong Zhang1
Junxue Zhang1, Wei Bai1, Kai Chen1, Mosharaf Chowdhury2

## Slide 2
Datacenter networks --- multi-rooted trees (e.g., Fat-tree, Leaf-spine)
    Multiple-paths between each end host pair
    Precise load balancing is required
Background
Difficult because datacenters are filled with uncertainties
Switch & server icon source: CONGA [SIGCOMM’14]

## Slide 3
Traffic dynamics
  Congestions can quickly arise at any place
Uncertainties in Datacenter Networks

## Slide 4
Asymmetries
  Link cuts
  Heterogenous devices
Leaf
Spine
40G
10G
Uncertainties in Datacenter Networks
Link cut

## Slide 5
‘Gray failure’
Leaf
Spine
Uncertainties in Datacenter Networks
Switch Failures
  Packet blackholes: drop packets with certain patterns deterministically;
  Silent random packet drops: drops packets randomly at a high rate;

## Slide 6
‘Gray failure’
Leaf
Spine
Uncertainties in Datacenter Networks
Uncertainties: traffic dynamics, asymmetries, switch failures
Link cut
How to effectively and appropriately load balance traffic?
Notes: .

## Slide 7
efficiently sense congestion & failures
Sensing Uncertainties
appropriately split traffic among parallel paths in reaction to uncertainties
Reacting to Uncertainties
Prior arts have important drawbacks in both

## Slide 8
Sensing Congestion
  Congestion-oblivious
    ECMP, RPS[INFOCOM’09], DRB[CoNEXT’13], Presto[SIGCOMM’15]
  Congestion-aware
    Switch-based
    CONGA[SIGCOMM’14], HULA[SOSR’16], DRILL*[SIGCOMM’17]
    End host-based
    CLOVE-ECN[HotNets’16]
Sensing Failures
  Most current solutions do not sense failures
Sensing Uncertainties --- Current Practice
Advanced hardware
Poor under asymmetry
Limited visibility

## Slide 9
Problem of Being Failure-ignorant
Random drop
S0
S1
L0
L1
 | S0 | S1
L1 | 5 | 5
Dest Leaf
Path

## Slide 10
Random drop
S0
S1
L0
L1
 | S0 | S1
L1 | 2 | 5
Dest Leaf
Path
1
Problem of Being Failure-ignorant

## Slide 11
Random drop
Even worse than ECMP under failures
S0
S1
L0
L1
 | S0 | S1
L1 | 2 | 2
Dest Leaf
Path
Problem of Being Failure-ignorant

## Slide 12
Problem of flowlet switching
  --- CONGA[SIGCOMM’14], CLOVE[HotNets’16], LetFlow[NSDI’17], …
Reacting to Uncertainties --- Current Practice
    Flowlet gap
  Passive and conservative in order to preserve packet orders

## Slide 13
Problem of flowlet switching
Flow C, D finish
Flow C, D finish
Flow A, B finish
Time
P1
P2
Ideal
L0
L1
P1
P2
A
B
C
D
Flows
Cannot always timely react to uncertainties
Reacting to Uncertainties --- Current Practice
Flow C reroute from P2 to P1
Flow A, B finish
Time
P1
P2
CONGA (flowlet)
+ DCTCP
Cannot find a flowlet gap

## Slide 14
Problem of vigorous rerouting
  Packet reordering
  Congestion mismatch
What is congestion mismatch?
  Congestion control: adjust rates based on the congestion of the current path;
  With vigorous rerouting: congestion states of different paths are mixed together;
Reacting to Uncertainties --- Current Practice
Congestion on one path may be mistakenly used to adjust the rate on another path

## Slide 15
Example of congestion mismatch
1G
1G
10G
10G
Flow A
DCTCP
S0
S1
L0
L1
Reacting to Uncertainties --- Current Practice
Start with high sending rate
Sending rate keeps increasing
10G
10 flowcells
1 flowcell
    fix sized data units
    Flowcell
    (Presto[SIGCOMM’15] )

## Slide 16
Example of congestion mismatch
1G
1G
10G
10G
Flow A
DCTCP
S0
S1
L0
L1
Reacting to Uncertainties --- Current Practice
10G
10 flowcells
1 flowcell
Rate reduce greatly
Start with low sending rate

## Slide 17
Example of congestion mismatch
1G
1G
10G
10G
Flow A
DCTCP
S0
S1
L0
L1
Reacting to Uncertainties --- Current Practice
10G
10 flowcells
1 flowcell
Cannot fully utilize 10Gbps
Severe queue build-up
Congestion mismatch leads to performance loss

## Slide 18
Comprehensiveness: effectively detect congestion and failures
Timeliness: quickly react to uncertainties
Transport-friendliness: limited impact of reordering and congestion mismatch
Deployability: implementable with commodity hardware
Q: Can we design a resilient load balancing scheme that can gracefully handle all these uncertainties?
Hermes

## Slide 19
Comprehensive Sensing
Leveraging Transport-layer signals & events
Active probing with small costs
Timely yet Cautious Rerouting
Explicitly consider both the cost and gain of rerouting
Hermes in One Slide
End host
Network Traffic
Hypervisor
Active Probing
Sensing Congestion
Probe
Sensing Module
Sensing Failures
Trigger
Endhost-based
--- No hardware/kernel modification
(Re)Routing Module
When & Where to reroute?
(Re)Route
Feed

## Slide 20
Comprehensive Sensing
Idea 1: Leveraging transport-level signals & events
Sensing Congestion
  ECN and RTT ----- widely used in congestion control, directly observable
Sensing Failures
  Packet blackhole
  Random packet drop
Failed paths
---- Frequent retransmission
--- Frequent timeout

## Slide 21
Comprehensive Sensing
Idea 1: Leveraging transport-level signals & events
Sensing Congestion
  ECN and RTT ----- widely used in congestion control, directly observable
Sensing Failures
  Packet blackhole
  Random packet drop
Failed paths
---- Frequent retransmission
--- Frequent timeout
Idea 2: Improving visibility via active probing
Baseline
Probe all paths for all endhost pairs
Power of 2 Choices
Probe 2 random +
1 previous best path
Sacrifice some visibility for much smaller probing overhead

## Slide 22
Timely yet Cautious Rerouting
When to reroute?
  Flowlet-switching: too conservative for timely reaction
  Vigorous-switching: too aggressive to be transport-friendly
Can we achieve a better trade-off by explicitly considering both the cost and gain of rerouting?
  A new angle: utility-based rerouting
    ----- reroute when it is likely to be beneficial
    final performance vs. intermediate consequences
Estimated based on both path conditions and flow status obtained from comprehensive sensing.

## Slide 23
Timely yet Cautious Rerouting
A simplified cost-benefit assessment for rerouting
Motivation for timely rerouting
Time
Rate
R1
R2
T1
T2
Remaining size = R1 T1
Do not reroute
0.5R1

## Slide 24
Quick reaction to uncertainties
Timely yet Cautious Rerouting
A simplified cost-benefit assessment for rerouting
Motivation for timely rerouting
Rerouting can be beneficial even with packet reordering;
Reroute immediately as long as it is likely to reduce flow completion time.
Time
Rate
R1
T1
T2
Remaining size = R1 T1
Do not reroute
T2
R2
Reroute
0.5R1

## Slide 25
Timely yet Cautious Rerouting
Time
Rate
R1
T1
Remaining size = R1 T1
Do not reroute
T2
R2
Reroute
0.5R1
Heuristics for cautious rerouting
Reroute only if new path is notably better (in terms of ECN&RTT);
A simplified cost-benefit assessment for rerouting
R2
Estimation
Error
Reroute
0.5R1
T2

## Slide 26
Timely yet Cautious Rerouting
Heuristics for cautious rerouting
Reroute only if new path is notably better (in terms of ECN&RTT);
Avoid rerouting flows with small remaining size;
A simplified cost-benefit assessment for rerouting
Time
Rate
R1
T1
Remaining size = R1 T1
Do not reroute
T2
R2
Reroute
0.5R1

## Slide 27
Timely yet Cautious Rerouting
Heuristics for cautious rerouting
Reroute only if new path is notably better (in terms of ECN&RTT);
Avoid rerouting flows with small remaining size;
Avoid rerouting flows with high sending rate R1;
A simplified cost-benefit assessment for rerouting
Time
Rate
R1
T1
Remaining size = R1 T1
Do not reroute
R2
R’2
Limited impact of congestion mismatch and packet reordering

## Slide 28
Workload
  Web-search
  Data-mining
Transport Protocol
  DCTCP
Evaluation Settings
Chart: Size (Bytes)
| 10 | 180 | 216 | 560 | 900 | 1100 | 1870 | 3160 | 10000 | 400000 | 3160000 | 100000000 | 1000000000
Web Search | 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 0.95 | 0.98 | 1
Data Mining | 0 | 0.15 | 0.2 | 0.3 | 0.4 | 0.53 | 0.6 | 0.7 | 0.8 | 0.9 | 0.97 | 1 | 1
Large Scale Simulations
  128 servers, 16 switches
  8X8 Leaf Spine with 2:1 oversubscription ratio
Testbed Evaluations
  12 servers, 4 switches
  2X2 leaf spine with 3:2 oversubscription ratio

## Slide 29
Hermes under baseline topology (8*8 leaf-spine)
Evaluation Results
Chart: Load (%)
| 30 | 50 | 70 | 90
ECMP | 23.159 | 28.769 | 38.193 | 38.407
CONGA | 18.191 | 22.137 | 27.972 | 28.476
HERMES | 18.028 | 21.787 | 26.34 | 26.664
Chart: Load (%)
| 30 | 50 | 70 | 90
ECMP | 3.921 | 5.852 | 10.531 | 28.887
CONGA | 3.086 | 4.012 | 5.908 | 15.513
HERMES | 3.426 | 4.579 | 7.043 | 18.549
Web-Search Workload
Outperforms ECMP by up to 55%
Within 17% of CONGA
Data-Mining Workload
29% better than ECMP at high load
slightly outperform CONGA (up to 4%)
More heavy tailed, less bursty, thus more difficult to create flowlet gaps
Switch-based solution has better visibility to congestion

## Slide 30
Hermes under asymmetric case (data-mining workload)
  Reduce the capacity from 10Gbps to 2Gbps for 20% of randomly selected leaf-to-spine links
Evaluation Results
Chart: Load (%)
| 30 | 40 | 50 | 60 | 70 | 80 | 90
CLOVE-ECN | 1.2408 | 1.1986 | 1.2387 | 1.2419 | 1.1903 | 1.1956 | 1.1492
CONGA | 1.12 | 1.081 | 1.0985 | 1.0983 | 1.0824 | 1.0889 | 1.0603
Hermes | 1 | 1 | 1 | 1 | 1 | 1 | 1
Presto* | 0.96663 | 0.99075 | 1.1009 | 1.1397 | 1.262 | 1.299 | 1.3378
LetFlow | 1.233 | 1.2206 | 1.1961 | 1.2082 | 1.2132 | 1.1749 | 1.1581
(Weighted) Presto*: congestion-oblivious, thus not efficient against asymmetry
CONGA: Hermes can more timely resolve collisions of large flows on 2Gbps links
LetFlow & CLOVE-ECN: Hermes has better visibility and more timely reaction

## Slide 31
Evaluation Results
Chart: Load (%)
| 30 | 40 | 50 | 60 | 70
ECMP | 10.825 | 11.303 | 12.035 | 14.181 | 17.274
CONGA | 10.221 | 10.705 | 12.614 | 13.022 | 15.268
Hermes | 4.727 | 5.223 | 6.029 | 7.602 | 10.589
Presto* | 18.169 | 18.135 | 20.833 | 21.808 | 26.264
LetFlow | 6.992 | 8.174 | 9.597 | 11.005 | 14.895
Chart: Load (%)
| 30 | 40 | 50 | 60 | 70
ECMP | 86.9 | 79.5 | 86.4 | 86.4 | 88.9
CONGA | 318.5 | 387.3 | 446.6 | 511.8 | 547
Hermes | 3.8 | 4.127 | 4.843 | 8.14 | 9.29
Presto* | 37.5 | 37.1 | 36.5 | 38.2 | 40.8
LetFlow | 6.4 | 7.835 | 9.4 | 13.7 | 16.8
Hermes under switch failures
Silent random packet drops
Packet blackhole
Outperform other schemes by over 32%

## Slide 32
Datacenter is filled with uncertainties
Hermes: a resilient load balancing scheme that gracefully handles uncertainties.
Conclusion
Readily-deployable at end hosts
Congestion & failure-aware
Improved visibility
Sensing
Reacting
Timely & Cautious rerouting

## Slide 33
Thank You!